## Slide 1: Cisco Secure Analytics
Formerly StealthWatch
Notes: https://www.cisco.com/c/en/us/products/collateral/security/stealthwatch/datasheet-c78-739398.html

## Slide 2: Agenda
What is Cisco Secure Analytics
Component of Secure Analytics
Installation of Secure Analytics
Notes: Watch : https://youtu.be/DPMGMIuJUfs

## Slide 3: What is Cisco Stealthwatch ?
Toolset to ingest, store, and analyze NetFlow
  GUI representation of NetFlow
  Algorithms for built-in security analysis
  Filtering, alerting, intuitive grouping of address space
  Appliances with different roles: generate, forward, store, query
Network Devices
Or Agents
Flow Sensor
CTB Broker
Flow Collector
Generate
Forward
Store
Query
Stealthwatch
Management
Console
SMC

## Slide 4: Secure Network Analytics Flow Collector
The Flow Collector leverages enterprise telemetry such as NetFlow, IPFIX (Internet Protocol Flow Information Export), and other types of flow data from existing infrastructure such as routers, switches, firewalls, endpoints, and other network infrastructure devices.
Customers can deploy Cisco Flow Collector using the following options:
Flow Collector 4210 is 1RU physical appliance (Part number: ST-FC4210-K9) which supports up to 65535 Interfaces, up to 4096 Exporters and up to 250,000-500,000 Flows per Second(fps).
Flow Collector 5210 is 1RU physical appliance (Part number: ST-FC5210-K9) which supports up to 65535 Interfaces, up to 4096 Exporters and up to 300,000 Flows per Second(fps).
Secure Network Analytics Flow Collector Virtual Edition can be configured as either FCVE-1000, FCVE-2000, or FCVE-4000—Part number: L-ST-FC-VE-K9.

## Slide 5: Secure Network Analytics Manager
The Secure Network Analytics Manager aggregates, organizes, and presents analyses from up to 25 Flow Collectors, Cisco Secure Network Access (formerly Cisco Identity Services Engine), and other sources. It uses graphical representations of network traffic, identity information, customized summary reports, and integrated security and network intelligence for comprehensive analysis.
The capacity of the manager determines the volume of telemetry data that can be analyzed and presented, as well as the number of Flow Collectors that are deployed. The manager is available as a hardware appliance or a virtual machine.